## Slide 2
Busy
Clear
Channel Status
Last Busy
Last Clear
Tquiet
Signal
Signal
Tquiet is time no signal detected before reporting channel is clear (nominal 1700 ms)
Last Busy or Last Clear updated internally approximately every 23 ms
Channel Busy Detector

## Slide 3
Busy
Clear
Channel Status
Last Clear
Signal (connect req from Client)
Leader
Tenb is time of Last Clear to Connect Request Frame ID.
If Tenb is > 500ms Connect request is blocked (server will not answer)
Busy Block Mechanism
Connect Req
Last Connect request
Tquiet
Tenb